## Slide 1
DIGITAL LOGIC DESIGN PROJECT
Design and Simulation of a Digital Even and Odd Parity Generator Using XOR Gates
Siva Nandan  2620030261
Yasashwini Chakali  2620030206
Krishnasree  2620030263
Akshara  2620030255 Hari Chandan Bongu  2620030271

## Slide 2
INTRODUCTION
Objective of the Project
Design a combinational circuit that generates a parity bit for a group of data bits, using XOR gates.
Implement both Even Parity and Odd Parity generation from the same core XOR logic.
Verify circuit correctness through a truth table and logic simulation.
Understand the role of parity in detecting single-bit transmission errors.
XOR
Why XOR Gates?
XOR outputs 1 only when its inputs differ — chaining them naturally counts whether the total number of 1s in a data word is odd or even.
Core Idea
Even parity: total 1s (data + parity bit) is even.
Odd parity: total 1s (data + parity bit) is odd.
2

## Slide 3
CONCEPT
What Is a Parity Bit?
A parity bit is an extra bit added to a data word before transmission so a receiver can detect single-bit errors caused by noise.
It is computed purely from the data bits — no external input is needed.
The receiver recomputes parity on arrival and compares it to the received parity bit; a mismatch signals an error.
1
0
1
1
+
1
Data Bits (A B C D)
Parity Bit
Example: data 1011 has three 1s (odd count). Adding parity bit = 1 makes the total four 1s — an even count. This is even parity.
3

## Slide 4
THEORY
The XOR Gate: The Right Tool for the Job
A | B | A ⊕ B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
XOR outputs 1 only when its two inputs differ.
Extended to many inputs, XOR computes the parity of the whole set: the output is 1 when the inputs contain an odd number of 1s.
That is exactly the property a parity generator needs — which is why cascaded XOR gates, not AND/OR combinations, are used.
XOR
A
B
A⊕B
Key Boolean Identity
Even parity bit: P = A ⊕ B ⊕ C ⊕ ... ⊕ N
Odd parity bit: P' = NOT ( A ⊕ B ⊕ C ⊕ ... ⊕ N )
4

## Slide 5
DESIGN
Truth Table — 3-Bit Data Word (A, B, C)
A | B | C | A⊕B⊕C | Even Parity (P) | Odd Parity (P')
0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 1 | 1 | 0
0 | 1 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0 | 1
1 | 1 | 0 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1 | 0
Even parity bit P = A⊕B⊕C • Odd parity bit P' = NOT(P)
5

## Slide 6
CIRCUIT DESIGN
Even Parity Generator — Logic Diagram
4-bit example: cascaded XOR gates compute P = A ⊕ B ⊕ C ⊕ D
A
B
C
D
XOR
A⊕B
XOR
XOR
Even Parity Output P
3 XOR gates are needed to combine 4 data bits (n−1 gates for n bits). Each gate's output feeds the next stage, cumulatively tracking whether the number of 1s seen so far is odd or even.
6

## Slide 7
CIRCUIT DESIGN
Odd Parity Generator — Logic Diagram
Same XOR cascade, with one inverter (NOT) added at the final stage
XOR Cascade
(A ⊕ B ⊕ C ⊕ D)
(as built on the previous slide)
NOT
Odd Parity Output P'
Equivalently, the last XOR gate in the cascade can be replaced directly with an XNOR gate — producing P' in a single extra step instead of a separate NOT gate.
7

## Slide 8
IMPLEMENTATION
HDL Implementation (Verilog)
4-bit even and odd parity generator, ready for simulation in ModelSim / Vivado / Quartus
module parity_generator(
input [3:0] data,
output even_parity,
output odd_parity
);
assign even_parity = data[0] ^ data[1] ^ data[2] ^ data[3];
assign odd_parity = ~(data[0] ^ data[1] ^ data[2] ^ data[3]);
endmodule
The XOR chain (^) mirrors the cascaded-gate diagram exactly; the tilde (~) implements the final NOT for odd parity.
8

## Slide 9
SIMULATION
Tools Used for Simulation
1
Logisim Evolution
Drag-and-drop gate simulation; ideal for verifying the truth table visually.
2
Multisim / Proteus
Realistic circuit simulation with waveform and timing-diagram output.
3
ModelSim / Vivado / Quartus
HDL simulation and synthesis of the Verilog design for FPGA targets.
4
Tinkercad Circuits
Free browser-based option for quick visual demonstrations.
9

## Slide 10
SIGNIFICANCE
Applications of Parity Generation
1
Serial Communication
UART and other serial links use parity bits to catch single-bit transmission errors.
2
Memory Systems
RAM and cache use parity checking as a lightweight integrity check on stored data.
3
RAID Storage
Basic redundancy and error checking in disk-array storage systems.
4
Foundation for Advanced Codes
Underlies more powerful error-correcting schemes such as Hamming codes and CRC.
10

## Slide 11
CONCLUSION
A Simple Gate, A Powerful Guarantee
Cascaded XOR gates compute data parity in the minimum possible number of gates (n−1 for n bits).
Even and odd parity generators share the same core circuit, differing only by a single inverter.
The design was verified by truth table and is ready for gate-level and HDL simulation.
This forms the building block for real-world error detection in communication and storage systems.